## Slide 1
PRISM · Phase 3 integration
Implementation, measured results and remaining validation
23 October 2026 · Advisory prototype
Notes: Implementation evidence from the PRISM Phase 3 branch, 23 October 2026. See docs/PHASE3_COMPLETION.md and reports/phase3_*.json.

## Slide 2
Reference topology
66 canonical assets
50 qualifying Delhi asset identities meet the report’s reference count.
245 dated circuit observations and 16 interface assertions remain inspectable.
49 source station labels map to loading measurements; 17 assets have no eligible feed.
Reference identity and source coverage do not certify current switching, line limits or electrical simulation readiness.
Notes: Sources: data/topology/delhi/RECONCILIATION.md; reports/phase3_station_feed.json. All metrics are limited to their declared source, workload and evaluation protocol.

## Slide 3
Real demand history
720 of 730 days captured
203,870 valid five-minute observations support 16,965 eligible hourly means.
555 missing or insufficient hours remain missing.
Raw fingerprints, UTC conversion and PostgreSQL rows preserve the audit trail.
Citywide Delhi demand only. Audited real solar/wind histories remain unavailable.
Notes: Sources: reports/phase3_history_audit.json. All metrics are limited to their declared source, workload and evaluation protocol.

## Slide 4
24-hour demand forecasts
Autoregression leads this evaluation
46 held-out daily origins · 1,104 frozen forecast hours · RMSE in MW
LSTM misses the normalized error targets. Empirical 90% bands have measured coverage, not a guarantee.
Chart: 
| Persistence | Autoregression | LSTM
RMSE (MW) | 732.42 | 426.54 | 758.4
Notes: Sources: reports/phase3_real_forecasting.json; reports/phase3_metrics.json. All metrics are limited to their declared source, workload and evaluation protocol.

## Slide 5
Policy and explanations
97.62% held-out policy agreement
Six-action XGBoost imitates the frozen synthetic Q-policy.
TreeSHAP explains the actual surrogate score using 100 training samples.
The interface exposes disagreements and score-based abstention.
Fidelity does not establish dispatch quality. Q-policy cost is 14.44% higher than the synthetic rule baseline.
Notes: Sources: reports/phase3_surrogate.json; reports/phase3_explanations.json; reports/phase3_metrics.json. All metrics are limited to their declared source, workload and evaluation protocol.

## Slide 6
Advisory operations
Explicit human review
Background scenarios support status, cancellation, retries and recovery.
Accepted and overridden advice records the operator label, reason and model evidence.
Graph paths and alarm timing produce investigation hypotheses.
Decisions send no equipment commands. Operator labels and software tests are not operator-survey evidence.
Notes: Sources: reports/phase3_operations.json; docs/OPERATIONS.md. All metrics are limited to their declared source, workload and evaluation protocol.

## Slide 7
Deployment and retraining
Seven services verified locally
Gunicorn, worker, scheduler, collector, Redis, PostgreSQL and Neo4j run together.
A candidate without sufficient validation improvement retains the current model.
Atomic version pointers support promotion and rollback.
Observed 8 GB host; every component stayed below 4 GB in a short test. Long-term availability remains unmeasured.
Notes: Sources: reports/phase3_deployment.json; reports/phase3_resources.json; reports/phase3_retraining.json. All metrics are limited to their declared source, workload and evaluation protocol.

## Slide 8
Remaining validation and demo
Research acceptance remains separate
Current electrical parameters and physical cascade/frequency validation
Audited renewable history and improved learned-policy outcomes
Qualified operator feedback and long-term service availability
Demo: inspect reference → check source age → forecast → run scenario → review explanation → record advisory decision → inspect hypotheses
Notes: Sources: docs/PHASE3_COMPLETION.md; docs/PHASE3_DEMO.md. All metrics are limited to their declared source, workload and evaluation protocol.